INSTALLATION INSTRUCTIONS

STEERING BOX

PLEASE READ INSTRUCTIONS BEFORE INSTALLATION

1) Remove original steering box and mounting brackets.

2) Install 7/16" studs into the steering box per drawing. Note: 7/16"x 2" long stud will be installed on the upper rear mounting hole. Use of Lockite is recommended.

3) Locate the (3) .700" thick sleeves. Place these sleeves over the 7/16 studs that are 2 1/2" long. One sleeve (.275" thick) will be placed over the 7/16" stud that is 2" long. As the steering box is placed on the Big Daddy Offroad Steering Box Mount, the 7/16" stud that is 2" long will need to be started first! Next, torque all (4) 7/16" lock-nuts to 65 ft-lb.

4) Place the steering box and Big Daddy Offroad Mount onto the original mounting holes in the chassis; torque the 5 nuts to 55 ft-lb each. Next, place the 5/8" x 2 1/2" bolt through the side of the frame and into the hole that corresponds with the nut that is welded into the BDOR steering mount.

5) Finally, replace the steering shaft, pitman arm, and the power steering lines.

Big Daddy Offroad

3134 NC 89 E, Walnut Cove NC 27052; Ph 336-591-1108